Dispensa-Matic Label Dispensers

28220 Playmor Beach Road

Rocky Mount, MO 65072

573 392-7684   Fax 573 392-1757

Toll Free: 1 800 325-7303

On line at: www.dispensamatic.com

Bottle-Matic 10” Specifications

For applying labels to cylindrical container up to 9” long (or longer if item has a neck)

Size:					15”x 17”x 8” (LxWxH)  (Machine only- does not include label roll)

Weight: 				17 lbs (Packaged weight 32 pounds)

Voltage: 				115v/ 220v

Container Diameter:		1/2” to 10”*

Label Requirements:		Die cut labels printed in copy position # 3 or #4.

Minimum width of backing paper should be 11/2”

Must have 1/8 gap between labels and 3” core.

Label Width: 			½” to 8”

Label Length: 			½” to 25”

Labeling Speed: 			4 ½” plus per second

Production per Hour:		1000 pieces using a 7” long label **

Label Thickness: 	Most labels 4 mil or thicker, and also most Mylar, foil and acetate labels.

Max Roll Diameter:  		 Standard: 9”, with optional Large roll adaptor 15”

Max Roll Weight: 		None

Actuation: 			Semi-automatic with foot switch and solid state controls

(push button optional – no additional charge)

Warranty: 				3 year parts & labor

* Smaller diameter(less than 1.5”) or lighter weight empty plastic bottles may require the use of the pressure arm – included with machine.

** Actual production will depend on operator efficiency in placing and removing containers

to be labeled.

Rv 12/2010