Dispensa-Matic Label Dispensers

28220 Playmor Beach Road

Rocky Mount, MO 65072

573 392-7684   Fax 573 392-1757

Toll Free: 1 800 325-7303

On line at www.dispensamatic.com

U-45HS (high speed) Specifications

For roll or fan fold labels longer than 4” and up to 4 ½” wide

Size: 					10”x 10” x 8” (LxWxH)  Machine only- does not include label roll

Weight: 				11 lbs

Voltage: 				115v or 220v

Dispensing Speed: 		11 inches per second

Label Width: 			3/8” to 4 1/2”

Label Length:	 		4 ”+*

Label Thickness:	Paper labels thicker than 3 MIL. For Mylar, foil, acetate or very thin labels use of the optional sharp edge dispensing table and/or micro-switch guide may be required.

Max. Roll Diameter:**  	Standard: 9” with optional roll adaptor: 15”

Max. Roll Weight: 		10 lbs

Actuation: 				Automatic w/Photo Eye (micro-switch available upon request)

Warranty: 				3 year parts & labor

*Labels less than 4” will dispense properly, but the high speed operation of the machine may not be beneficial for shorter labels and a standard U-45 is recommended

** One up fan fold label formats can also be used