Dispensa-Matic Label Dispensers

28220 Playmor Beach Road

Rocky Mount, MO 65072

573 392-7684   Fax 573 392-1757

Toll Free: 1 800 325-7303

DM-II Series Specifications

10-II

Recommended for large roll labels, either butt cut or die cut and 1-up fan fold forms

Size: 					15” x 10” x 7”  (LxWxH) Machine only- does not include label roll

Weight: 				13 lbs

Voltage: 				115v or 220v

Dispensing Speed: 		5 inches per second

Label Width: 	1” to 8” on rolls, 1” to 9” fanfolded

Label Length: 			½” to 12+”*

Label Thickness:                      Paper labels thicker than 3 MIL should dispense properly. For

Mylar, foil, acetate or very thin labels use of the optional sharp edge dispensing table and/or micro-switch guide may be required

Max Roll Diameter:  		Standard: 9” with optional roll adaptor: 15”

Max Roll Weight: 		10 lbs.

Actuation: 				Photo eye (Microswitch available upon request)

Warranty: 				3 year parts & labor